## Slide 1
Style：Simple
Size： Middle tower support up to ATX MB
Material： Steel & Plastic & Tempered Glass
Main Feature
Connection ： Top-Front I/O ports with 1 x USB 3.0, 2 x USB 2.0
Ventilation ： 1 preinstalled 120mm fan
Support ：Advance Cable Management
Thermaltake Versa T25 TG Middle tower

## Slide 2
Model | Versa T25 TG w/600W PSU
P/N | CA-3R5-60M1WG-00
Case Type | Middle tower
Chassis Dimension (H*W*D) | 416 x 210 x 480 mm (16.38 x 8.27 x 18.9 inch)
Net Weight(Case) | 6.65 kg / 14.66 lbs.
Side Panel | 4mm Tempered Glass x2(Left & Front)
Color | Exterior & Interior : Black
Material | SPCC
Cooling System | Rear (exhaust) : 1 x 120 x 120 x 25 mm fan (1000rpm, 16 dBA)
Drive Bays -Accessible -Hidden | 2 x 3.5“ or 2.5” (HDD Rack); 2 x 2.5” (HDD Bracket)
Expansion Slots | 7
Motherboards | 6.7” x 6.7” (Mini ITX), 9.6” x 9.6” (Micro ATX), 12” x 9.6” (ATX)
I/O Port | 1 x USB 3.0, 2 x USB 2.0, 1 x HD Audio,
PSU | PS-TTP-0600NNFANG-1
Fan Support | Front: 3 x 120mm or 2 x 120mm or 1 x 120mm 2 x 140mm or 1 x 140mm 2 x 200mm or 1 x 200mm Top: 2 x 120mm or 1 x 120mm 2 x 140mm or 1 x 140mm Rear: 1 x 120mm,
Radiator Support | Front: 1 x 360mm or 1 x 240mm or 1 x 120mm 1x 280mm or 1 x 140mm Top: 1 x 240mm or 1 x 120mm Rear: 1 x 120mm
Clearance | CPU cooler height limitation: 150mm PSU length limitation: 160mm(With HDD Rack) 200mm(Without HDD Rack) VGA length limitation: 300mm RAM height limitation: 60mm(With radiator series)
Specification
Thermaltake Versa T25 TG Middle tower

## Slide 3
Packaging
Package Information | Versa T25 TG w/600W PSU
EAN Code | 4713227526906
UPC Code | 841163076910
N.W | 6.65 kg / 14.66 lbs.
G.W | 7.75 kg / 17.09 lbs.
Carton Size (L x W x H) | 536 x 272 x 480 mm / 21.1 x 10.7 x 18.9 inch
Cuft | 2.47
Container | W/O pallet
20’ | 360
40’ | 810
40’ HQ | 950
Thermaltake Versa T25 TG Middle tower

## Slide 4
Angle view
Rear view
Internal Structure
Top view
Left Side view
Front view
Right Side view
Bottom view
Appearance - CA-1R5-00M1WN-00
Thermaltake Versa T25 TG Middle tower

## Slide 5
Thermaltake Versa T25 TG Middle tower
Unique Design
Maximum radiator support up to 360mm
Maximum support up to 6 x 120 mm fan
2 x Tempered Glass
( Left & Front)

## Slide 6
Thermaltake Versa T25 TG Middle tower
Structure (External)
USB connector
One 120mm rear fan

## Slide 7
HDD expansion introduction
HDD Bracket
Thermaltake Versa T25 TG Middle tower

## Slide 8
HDD expansion introduction
Application
Thermaltake Versa T25 TG Middle tower

## Slide 9
Rear (exhaust) : 120 x 120 x 25 mm ARGB fan x 1 (1000rpm, 16dBA)
CPU Air Cooling System
A
The Cooling System – AIO Liquid Cooling (Optional)
A
B
HDD Air Cooling System
B
Front (intake) : 200 x 200 x 30 mm ARGB fan x 2 (600rpm, 29.2 dBA)
Thermaltake Versa T25 TG Middle tower

## Slide 10
Fan compatibility
Thermaltake Versa T25 TG Middle tower

## Slide 11
Radiator compatibility
Thermaltake Versa T25 TG Middle tower

## Slide 12
Compatibility List
Fan Compatibility List |  |  | 
 | 120mm | 140mm | 200mm
Front | 3 | 2 | 2
Top | 2 | 2 | -
Rear | 1 | - | -
Thermaltake Compatible Fan |  |  | 
 | 120mm | 140mm | 200mm
PURE FAN Series | ● | ● | ●
Riing FAN Series | ● | ● | ●
All-in-One Compatibility List (Water 3.0 and Floe series) |  |  |  |  |  | 
 | Performer | Pro | 240 Series | 360 Series | 140 Series | 280 Series
Front | ● | ● | ● | ● | ● | ●
Top | ● | ● | ● | - | - | -
Rear | ● | ● | - | - | - | -
Radiator Compatibility List |  |  |  |  |  | 
 | 120mm | 240mm | 360mm | 140mm | 280mm | 420mm
Front | ● | ● | ● | ● | ● | -
Top | ● | ● | - | - | - | -
Rear | ● | - | - | - | - | -
Thermaltake Versa T25 TG Middle tower